| Video |
| --- |
| Number/signal type | 1 or 2 sets of proprietary analog signals |
| Connectors | 1 or 2 shielded RJ-45 female |
| Video output |
| Number/signal type |  |
| TP R BNC A | 1 analog RGBHV, RGBS, RGsB, component video, or S-video; or |
|  | 1 S-video and 1 NTSC/PAL/SECAM composite video from a single source; or |
|  | 3 NTSC/PAL composite video from a single source |
| TP R BNC AV | 1 analog RGBHV, RGBS, RGsB, component video, or S-video; or |
|  | 1 S-video and 1 NTSC/PAL/SECAM composite video from a single source; or |
|  | 3 NTSC/PAL/SECAM composite video from a single source |
|  | and 1 NTSC/PAL/SECAM composite video |
| TP R 15HD A | 1 analog RGBHV, RGBS, RGsB, component video, or S-video; or |
|  | 1 S-video and 1 NTSC/PAL/SECAM composite video from a single source; or |
|  | 3 NTSC/PAL composite video from a single source |
| TP R AV | 1 NTSC/PAL/SECAM composite video |
| Connectors |  |
| TP R BNC A | 5 BNC female |
| TP R BNC AV | 6 BNC female |
| TP R 15HD A | (1)15-pin HD female |
| TP R AV | 1 BNC female |
| Nominal level | 1V p-p for Y of component video and S-video, and for composite video |
|  | 0.7V p-p for RGB |
|  | 0.3V p-p for R-Y and B-Y of component video, and for C of S-video |
| Minimum/maximum levels | 0.3V to 1.45V p-p |
| Impedance | 75 ohms |
| Audio |
| Number/signal type | 1 or 2 sets of analog proprietary signals |
| Connectors | 1 or 2 shielded RJ-45 female |
| Frequency response | 20 Hz to 20 kHz, >±0.05dB |
| THD + Noise | 0.03% @ 1 kHz, 0.3% @ 20 kHz at rated maximum output drive |
| S/N | >63dB at nominal level |
| Crosstalk | <-80dB @ 1 kHz, fully loaded |
| Stereo channel separation | >80dB @ 1 kHz |
| CMRR | >33dB @ 20 Hz to 20 kHz |
| Audio output |
| Number/signal type |  |
| TP R BNC A, TP R AV | 1 stereo audio balanced/unbalanced, and 1 stereo audio unbalanced |
| TP R 15HD A | 1 stereo audio balanced/unbalanced |
| TP R BNC AV | 2 stereo audio balanced/unbalanced, and 2 stereo audio unbalanced |
| Connectors |  |
| TP R 15HD A | (1) 3.5 mm, 5-pole captive screw connector per input |
| All other models | 2 female RCA (left/right) per input |
|  | (1) 3.5 mm, 5-pole captive screw connector per input |
| Impedance | 50 ohms unbalanced, 100 ohms balanced |
| Gain error | ±0.1dB channel to channel |
| Maximum level (600 ohm) | >+11.5dBm, balanced at stated %THD+N |
| General |
| Power |  |
| TP R BNC A, TP R AV | 15VDC, 0.8 A, external power supply.: Product requires 0.3 A (minimum). |
| TP R 15HD A | 15VDC, 0.8 A, external power supply.: Product requires 0.34 A (maximum). |
| TP R BNC AV | 100VAC to 240VAC, 50/60 Hz, 40 watts, internal |
| Temperature/humidity | Storage -40° to +158°F (-40° to +70°C) / 10% to 90%, non-condensing |
|  | Operating +32° to +122°F (0° to +50°C) / 10% to 90%, non-condensing |
| Rack mount |  |
| TP R AV | No, but projector mountable with optional mounting kit (#70-077-04), |
|  | furniture mountable with optional mounting brackets (#70-077-01 and #70-077-02). |
| TP R 15HD A | Yes, with optional VersaTools 1U rack shelf, part #60-190-20 or optional |
|  | standard 1U rack shelf, part #60-190-01.: Also, projector mountable with optional |
|  | mounting kit, part #70-217-01 or under-furniture mountable with optional |
|  | mounting brackets, part #70-212-01. |
| TP R BNC A, TP R BNC AV | Yes, with optional 1U rack shelf, part #60-190-01.: Also, projector mountable |
|  | with optional mounting kit, part #70-077-04 or furniture mountable with |
|  | optional mounting brackets #70-077-01, 70-077-02. |
| Enclosure type | Metal |
| Enclosure dimensions |  |
| TP R BNC A | 1.3" H x 8.75" W x 7.0" D: (<1U high, half rack width) |
|  | 3.3 cm H x 22.2 cm W x 17.8 cm D |
|  | (Depth excludes connectors.) |
| TP R BNC AV | 1.7" H x 8.75" W x 7.0" D: (1U high, half rack width) |
|  | 4.3 cm H x 22.2 cm W x 17.8 cm D |
|  | (Depth excludes connectors.) |
| TP R 15HD A | 1.6" H x 4.25" W x 3.0" D: (1U high, |
|  | quarter rack width) |
|  | 4.1 cm H x 10.8 cm W x 7.6 cm D |
|  | (Depth excludes connectors.) |
| TP R AV | 1.25" H x 4.75" W x 7.0" D |
|  | 3.2 cm H x 12.1 cm W x 17.8 cm D |
|  | (Depth excludes connectors.) |
| Product weight |  |
| TP R BNC A | 1.6 lbs (0.7 kg) |
| TP R BNC AV | 2.6 lbs (1.2 kg) |
| TP R 15HD A | 0.4 lbs (0.2 kg) |
| TP R AV | 0.9 lbs (0.4 kg) |
| Shipping weight |  |
| TP R BNC A | 4 lbs (1.8 kg) |
| TP R BNC AV | 5 lbs (2.3 kg) |
| TP R 15HD A | 2 lbs (0.9 kg) |
| TP R AV | 3 lbs (1.4 kg) |
| Vibration | ISTA/NSTA 1A in carton (International Safe Transit Association) |
| Listings | UL, CUL |
| Compliances | CE, FCC Class A |
| MTBF | 30,000 hours |
| Warranty | 3 years parts and labor |